## Slide 1
NON-WSQ COURSE | EMBEDDED SYSTEMS
Arduino Masterclass
Course Code C218
Non-WSQ commercial short course
Conducted by Tertiary Infotech Academy Pte Ltd | UEN 201200696W
SENSE
DECIDE
ACT
Version 1.0 | 30 September 2026
Trainer: ______________________________

## Slide 2
TRAINER PROFILE
About the Trainer - Template
Name
________________________________________
Qualifications
________________________________________
Industry practice
________________________________________
Contact
________________________________________
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
2

## Slide 3
NAMED TRAINER PROFILE
About the Trainer - Dr Alfred Ang
Role
Principal Trainer, Tertiary Infotech Academy Pte Ltd
Engineering lens
Embedded systems, automation, software and applied AI
Teaching approach
Mechanism first: build, measure, diagnose, then improve
Learner evidence
Working circuits, readable sketches, serial traces and acceptance checks
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
3

## Slide 4
CONTEXT MAP
Let's Know Each Other
Your role
Where do electronics or automation show up in your work?
Prior exposure
Arduino, C/C++, breadboards, sensors, motors - any level is welcome.
Target build
What real device would you like to sense or control?
Evidence habit
How will you prove a prototype works rather than merely looks complete?
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
4

## Slide 5
WORKING AGREEMENT
Ground Rules
Safety first
Power OFF before rewiring. Never drive a motor directly from an I/O pin.
One circuit at a time
Build, inspect, power, measure, and record evidence before extending.
Active participation
Predict the output, explain the mechanism, then run the test.
Professional conduct
Respect others, return on time, and keep phones silent.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
5

## Slide 6
APPROVED COURSE DESIGN
Course Facts and Time Budget
Course
Arduino Masterclass
Duration
One day: 7.5 instructional hours (9:30am - 5:30pm)
Progress checks
Lab acceptance tests after every topic - no formal exam
Hardware
Arduino Uno/Maker UNO, breadboard, sensors, driver stages and actuators
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
6

## Slide 7
ONE CONTINUOUS CONTROL STACK
Course Learning Flow
1
Topic 1
Board, sketch, timing, serial
2
Topic 2
Voltage, current, digital I/O, PWM
3
Topic 3
ADC, calibration, LDR, servo
4
Topic 4
Ultrasonic, PIR, timeouts
5
Topic 5
DHT, drivers, motors, feedback
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
7

## Slide 8
SAFETY CONTROL POINTS
Equipment and Electrical Safety
I/O boundary
Use logic pins for signals, not motor/servo supply current.
Power boundary
External actuator power must share a common ground with Arduino.
Inductive loads
Use a transistor/MOSFET driver and flyback diode.
Rewire safely
Disconnect power before moving components or probing continuity.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
8

## Slide 9
VISUAL COURSE-PORTAL PATH
Download Course Material
1
SIGN IN
Open lms-tms.tertiaryinfotech.com
2
OPEN COURSE
Select C218
3
DOWNLOAD
Learner Slides, LG and Labs
4
VERIFY
Filename/version match v1.0
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
9

## Slide 10
01
TOPIC 1
Introduction to Embedded Systems
Architecture, resource constraints, ATmega328P, sketch lifecycle, timing, and serial evidence
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
10

## Slide 11
SIGNAL / CONTROL FLOW
Closed-Loop Embedded System
1
SENSOR
Physical quantity -> electrical signal
2
INPUT
ADC / digital threshold / serial frame
3
PROCESS
State + decision + timing
4
OUTPUT
GPIO / PWM / driver signal
5
EVIDENCE
Serial trace + measured behaviour
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
11

## Slide 12
DECISION / COMPARISON
General-Purpose vs Embedded Design
DESKTOP / MOBILE
Workload
Many user-selected applications
Resources
Large memory/storage; rich OS
Timing
Best effort is often acceptable
Power
Mains or large battery
EMBEDDED CONTROLLER
Workload
Dedicated control function
Resources
Bounded flash, SRAM and I/O
Timing
Deadlines affect physical behaviour
Power
Energy and thermal limits
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
12

## Slide 13
WORKED CALCULATION
Resource Budget Is a Design Contract
available = capacity - static - worst-case dynamic
SUBSTITUTE REAL VALUES
2,048 B SRAM - 820 B globals - 768 B stack margin = 460 B headroom
Flash
Sketch + libraries <= 32 KB
SRAM
Globals + heap + stack < 2 KB
Timing
Worst-case loop < control deadline
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
13

## Slide 14
TECHNICAL MODEL
ATmega328P Controller Map
CPU
8-bit AVR core at 16 MHz; executes the control program.
Memory
32 KB flash, 2 KB SRAM, 1 KB EEPROM - each has different persistence.
Interfaces
GPIO, ADC, timers/PWM, UART, SPI and I2C/TWI.
Reset / boot
Bootloader receives sketches; reset restarts setup() then loop().
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
14

## Slide 15
TECHNICAL MODEL
Arduino Uno Pin Budget
D0/D1
UART RX/TX - avoid conflicts while using Serial.
D3/5/6/9/10/11
PWM-capable on the classic Uno; timer use can interact with libraries.
A0-A5
Six 10-bit ADC channels; A4/A5 also serve I2C.
D13
Built-in LED - useful evidence without external wiring.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
15

## Slide 16
SIGNAL / CONTROL FLOW
Sketch Runtime Lifecycle
1
RESET
Registers/peripherals start from reset state
2
BOOTLOADER
Short upload/listen window
3
setup()
One-time pin, serial and library initialisation
4
loop()
Repeated control cycle
5
INTERRUPTS
Asynchronous events alter timing/state
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
16

## Slide 17
TECHNICAL MODEL
Variables Are Hardware-Relevant
uint8_t
Exact 0-255 range; matches many registers and PWM values.
int
Convenient arithmetic but size is architecture-dependent.
unsigned long
Holds millis()/micros() timestamps without negative values.
const
Documents a fixed pin/threshold and lets the compiler protect intent.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
17

## Slide 18
DECISION / COMPARISON
Blocking vs Scheduled Timing
BLOCKING
delay()
Stops normal loop progress
Consequence
Serial/button work waits
Use
Simple isolated demonstrations
Risk
Missed events and slow response
NON-BLOCKING
millis() delta
Checks elapsed time without stopping
Consequence
Multiple behaviours interleave
Use
Responsive control systems
Risk
Must handle rollover-safe subtraction
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
18

## Slide 19
TIMING WAVEFORM
UART Frame and Baud Contract
TX idle/start/data
55%
9600 bit/s budget
35%
Line terminator
75%
Sender and receiver must agree on baud, framing and line termination; otherwise text may be garbled or commands remain buffered.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
19

## Slide 20
RUNNABLE CODE CONTRACT
Line-Oriented Serial Parser
String command; bool ledOn = false; void applyOutput() { digitalWrite(LED_BUILTIN, ledOn ? HIGH : LOW); } void setup() { pinMode(LED_BUILTIN, OUTPUT); applyOutput(); Serial.begin(9600); Serial.println("READY: ON | OFF | STATUS"); } void loop() { if (Serial.available() == 0) return; command = Serial.readStringUntil('\n'); command.trim();
READ THE EVIDENCE
1
readStringUntil('\n') defines one command frame
2
trim() removes CR/LF residue
3
Unknown commands return ERR without changing output
4
Maintained ledOn state makes STATUS truthful
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
20

## Slide 21
OBSERVE -> COMPARE -> DECIDE
Upload and Runtime Diagnosis
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Compile
Binary produced
Compiler errors
Fix syntax/library
Port open
Board enumerates
No serial port
Cable/driver/permissions
Upload
avrdude success
Timeout / sync error
Board/port/reset
Runtime
Expected LED/Serial trace
Wrong output
State/timing/wiring
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
21

## Slide 22
PRACTICE BRIDGE | LO1
Lab 1: Board Check and Deterministic Blink
MECHANISM TO PROVE
Validate the Arduino Uno/Maker UNO toolchain and prove deterministic digital output timing.
DELIVERABLE
A board-identification record and a 250 ms LED heartbeat that verifies compile, upload, reset, and loop execution.
INPUT
LED_BUILTIN
CONTROL
const uint8_t LED_PIN = LED_
OUTPUT
Sketch compiles with no error
VERIFY
Measured ten-cycle duration is approximately 5 seconds
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
22

## Slide 23
RUNNABLE CODE CONTRACT
Lab 1 Evidence Code
const uint8_t LED_PIN = LED_BUILTIN; const unsigned long INTERVAL_MS = 250; void setup() { pinMode(LED_PIN, OUTPUT); } void loop() { digitalWrite(LED_PIN, HIGH); delay(INTERVAL_MS); digitalWrite(LED_PIN, LOW); delay(INTERVAL_MS); }
READ THE EVIDENCE
1
LED_BUILTIN avoids board-specific hard-coding
2
pinMode establishes the output contract
3
HIGH/LOW create two observable states
4
Timing evidence is measured across ten cycles
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
23

## Slide 24
OBSERVE -> COMPARE -> DECIDE
Lab 1 Acceptance and Failure
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Compile/upload
No errors
Pass/fail log
Fix toolchain before wiring
Period
500 ms per cycle
Ten cycles approx 5 s
Check millisecond units
Reset
Heartbeat restarts
Visible reset sequence
Confirms setup() reruns
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
24

## Slide 25
PRACTICE BRIDGE | LO1
Lab 2: Serial Command Control
MECHANISM TO PROVE
Trace UART data from a typed ASCII command to a validated output state.
DELIVERABLE
A line-oriented command parser that accepts ON, OFF, and STATUS without blocking indefinitely.
INPUT
LED_BUILTIN
CONTROL
String command;
OUTPUT
ON lights the LED
VERIFY
Unknown input returns ERR without changing output
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
25

## Slide 26
EDITABLE STATE MACHINE
Lab 2 Command State
OFF
safe default
ON
LED HIGH
REPORT
no state change
ON
OFF
STATUS
STATUS
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
26

## Slide 27
OBSERVE -> COMPARE -> DECIDE
Lab 2 Acceptance and Failure
TEST
EXPECTED
OBSERVED
DECISION / ACTION
ON
LED=ON + light
Observed trace
State and output agree
OFF
LED=OFF + dark
Observed trace
State and output agree
BAD
ERR, no change
Observed trace
Parser rejects safely
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
27

## Slide 28
02
TOPIC 2
Introduction to Basic Electronics
Voltage, current, resistance, breadboards, digital thresholds, pull-ups, debounce, PWM, and protected loads
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
28

## Slide 29
WORKED CALCULATION
LED Current-Limit Resistor
R = (Vsource - Vf) / I
SUBSTITUTE REAL VALUES
R = (5.0 V - 2.0 V) / 0.010 A = 300 ohm -> choose 330 ohm
Voltage
Resistor drops about 3 V
Current
About 9 mA with 330 ohm
Power
P = I^2R approx 0.027 W
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
29

## Slide 30
DECISION / COMPARISON
Series vs Parallel Circuits
SERIES
Current
Same current through each element
Voltage
Drops add to source voltage
Open fault
Breaks the whole path
Example
LED + current-limit resistor
PARALLEL
Voltage
Same voltage across branches
Current
Branch currents add
Open fault
Other branches may continue
Example
Multiple independently driven loads
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
30

## Slide 31
TECHNICAL MODEL
Breadboard Connectivity
Terminal strips
Groups of five holes are internally common; the centre gap isolates sides.
Power rails
Long rails distribute supply but may be split mid-board.
Cross-check
Use continuity mode before power when rail segmentation is uncertain.
Failure signature
Same-row component legs can short a device or bypass a resistor.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
31

## Slide 32
TECHNICAL MODEL
Polarity and Component Boundaries
LED
Anode to controlled positive path; cathode to return.
Diode
Cathode band identifies direction; flyback diode is reverse-biased normally.
Electrolytic capacitor
Observe + and - markings; reverse polarity can damage the part.
Transistor/MOSFET
Pin order varies by device; verify the datasheet, not package appearance.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
32

## Slide 33
TECHNICAL MODEL
Digital Input Thresholds
LOW
Voltage below the input-low threshold is read as logic 0.
HIGH
Voltage above the input-high threshold is read as logic 1.
Undefined region
Intermediate voltage is not a valid logic contract.
Floating
An unconnected high-impedance input can pick up noise and change randomly.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
33

## Slide 34
SIGNAL / CONTROL FLOW
INPUT_PULLUP Signal Path
1
INTERNAL RESISTOR
Weak pull-up connects input to VCC
2
RELEASED
Input reads HIGH
3
PRESSED
Switch connects input to GND
4
SOFTWARE
Interpret LOW as active
5
EVIDENCE
Raw + debounced states
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
34

## Slide 35
TIMING WAVEFORM
Mechanical Bounce vs Debounced State
Raw switch
48%
30 ms stable window
75%
Accepted press
25%
The controller accepts a new state only after the raw input remains unchanged for the debounce interval.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
35

## Slide 36
RUNNABLE CODE CONTRACT
Edge Detection and Debounce
const uint8_t BUTTON_PIN = 2; const uint8_t LED_PIN = 7; const unsigned long DEBOUNCE_MS = 30; bool ledOn = false; bool stableState = HIGH; bool lastRaw = HIGH; unsigned long changedAt = 0; void setup() { pinMode(BUTTON_PIN, INPUT_PULLUP); pinMode(LED_PIN, OUTPUT); } void loop() { bool raw = digitalRead(BUTTON_PIN); if (raw != lastRaw) { changedAt = millis(); lastRaw = raw; } if (millis() - changedAt >= DEBOUNCE_MS && raw != stableState) { stableState = raw;
READ THE EVIDENCE
1
lastRaw detects any electrical transition
2
changedAt records when stability began
3
stableState changes only after 30 ms
4
Only the confirmed falling edge toggles the LED
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
36

## Slide 37
TIMING WAVEFORM
PWM Duty Cycle
64 / 255
25%
128 / 255
50%
192 / 255
75%
On the classic Uno, analogWrite() produces PWM on supported pins; it is not a true analogue voltage.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
37

## Slide 38
TECHNICAL MODEL
Uno PWM and Timer Boundaries
8-bit command
analogWrite value 0-255 maps to 0-100% duty cycle.
PWM pins
Classic Uno: D3, D5, D6, D9, D10, D11.
Timer sharing
Tone, Servo, and timing libraries can change timer availability/behaviour.
Load boundary
PWM pin drives a control input; a transistor stage drives higher current.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
38

## Slide 39
SIGNAL / CONTROL FLOW
Protected Inductive Load
1
GPIO/PWM
Low-current logic signal
2
GATE/BASE
Current-limited drive
3
MOSFET/TRANSISTOR
Switches motor current
4
FLYBACK DIODE
Clamps inductive voltage
5
SUPPLY
Separate load energy + common ground
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
39

## Slide 40
PRACTICE BRIDGE | LO2
Lab 3: Safe LED Circuit and Ohm's Law
MECHANISM TO PROVE
Calculate and build a current-limited LED circuit within an Arduino digital pin's electrical boundary.
DELIVERABLE
A documented 5 V digital-output circuit using a 330 ohm resistor and measured LED voltage.
INPUT
D7
CONTROL
const uint8_t LED_PIN = 7;
OUTPUT
LED polarity is correct
VERIFY
Calculated current remains close to or below 10 mA
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
40

## Slide 41
OBSERVE -> COMPARE -> DECIDE
Lab 3 Electrical Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
R calc
300 ohm minimum target
330 ohm fitted
Safe standard value
LED Vf
Approx 1.8-2.2 V
Multimeter value
Use resistor voltage for current
I/O state
D7 HIGH/LOW
LED ON/OFF
Pin contract proven
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
41

## Slide 42
PRACTICE BRIDGE | LO2
Lab 4: Push Button with INPUT_PULLUP
MECHANISM TO PROVE
Eliminate a floating input and debounce a mechanical switch using a stable time window.
DELIVERABLE
An active-LOW button that toggles an LED once per physical press without double triggers.
INPUT
D2
CONTROL
const uint8_t BUTTON_PIN = 2
OUTPUT
Released input reads HIGH
VERIFY
Bounce within 30 ms does not create extra toggles
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
42

## Slide 43
EDITABLE STATE MACHINE
Lab 4 Debounced Button
RELEASED
HIGH
CANDIDATE
raw changed
PRESSED
LOW >30 ms
TOGGLED
one output change
edge
stable
falling
release
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
43

## Slide 44
PRACTICE BRIDGE | LO2
Lab 5: PWM Fade with Non-blocking Timing
MECHANISM TO PROVE
Relate 8-bit PWM values to duty cycle and vary LED brightness without blocking other logic.
DELIVERABLE
A triangular 0-255 PWM ramp on D9 with calculated duty-cycle checkpoints.
INPUT
D9 (~)
CONTROL
const uint8_t LED_PIN = 9;
OUTPUT
LED fades up and down continuously
VERIFY
Calculated 128 duty cycle is approximately 50%
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
44

## Slide 45
RUNNABLE CODE CONTRACT
Lab 5 Non-blocking PWM
const uint8_t LED_PIN = 9; const unsigned long UPDATE_MS = 20; const int STEP = 5; int brightness = 0; int direction = STEP; unsigned long lastUpdate = 0; void setup() { pinMode(LED_PIN, OUTPUT); } void loop() { if (millis() - lastUpdate < UPDATE_MS) return; lastUpdate = millis(); brightness += direction; if (brightness >= 255) { brightness = 255; direction = -STEP; } if (brightness <= 0) { brightness = 0; direction = STEP; } analogWrite(LED_PIN, brightness); }
READ THE EVIDENCE
1
Elapsed-time test keeps loop responsive
2
direction carries the ramp sign
3
Boundary clamp prevents wraparound
4
analogWrite commits the 8-bit duty value
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
45

## Slide 46
OBSERVE -> COMPARE -> DECIDE
Topic 2 Verification Matrix
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Digital output
Safe LED current
Measured resistor/Vf
Safe interconnection
Digital input
Stable active-LOW
Raw vs debounced trace
Signal conditioning
PWM
0-255 bounded ramp
Duty checkpoints
PWM mechanism
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
46

## Slide 47
03
TOPIC 3
Analogue Sensors and Transducers
Signal chains, 10-bit ADC, quantisation, calibration, filtering, LDR dividers, hysteresis, and servo control
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
47

## Slide 48
SIGNAL / CONTROL FLOW
Analogue Measurement Chain
1
PHYSICAL
Light / position / pressure
2
TRANSDUCER
Resistance or voltage changes
3
CONDITION
Divider, filter, reference
4
ADC
Voltage -> integer code
5
CONTROL
Calibrate, decide, command
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
48

## Slide 49
TECHNICAL MODEL
Continuous Signal, Discrete Code
Input
A0 accepts a voltage within the board's permitted range.
Sample
ADC observes the input at a point in time.
Quantise
The continuous value is assigned to one of 1024 codes.
Report
analogRead() returns an integer from 0 to 1023 on the classic Uno.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
49

## Slide 50
WORKED CALCULATION
10-bit ADC Conversion
Vin approx code x Vref / 1023
SUBSTITUTE REAL VALUES
code 614 at Vref 5.00 V -> Vin approx 3.00 V
Resolution
5 V / 1024 approx 4.88 mV per count
Range
Never exceed the allowed analogue input voltage
Reference
Measurement accuracy depends on actual Vref
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
50

## Slide 51
TECHNICAL MODEL
Reference Voltage and Accuracy
Default reference
Typically the board supply; USB/supply variation affects conversion.
Source impedance
High impedance can slow sample/hold settling.
Noise
Long wires and motors inject variation into ADC readings.
Calibration
Use measured endpoints rather than assuming ideal 0 and 1023.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
51

## Slide 52
RUNNABLE CODE CONTRACT
Moving-Average Filter
const int N = 8; long sum = 0; for (int i=0; i<N; i++) { sum += analogRead(A0); } int filtered = sum / N;
READ THE EVIDENCE
1
Eight independent samples contribute
2
long avoids sum overflow in larger windows
3
Division produces the mean code
4
Filtering reduces noise but adds latency
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
52

## Slide 53
WORKED CALCULATION
Calibrate and Map a Sensor
output = map(raw, rawMin, rawMax, outMin, outMax)
SUBSTITUTE REAL VALUES
map(constrain(raw, 180, 850), 180, 850, 0, 100)
Measure
Capture real minimum/maximum
Constrain
Reject out-of-range excursions
Validate
Compare mapped value to a reference
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
53

## Slide 54
WORKED CALCULATION
LDR Voltage Divider
Vout = Vcc x Rfixed / (RLDR + Rfixed)
SUBSTITUTE REAL VALUES
5 V x 10k / (30k + 10k) = 1.25 V in a darker condition
Orientation
Swapping LDR/fixed resistor reverses response
ADC
A0 observes divider junction
Threshold
Calibrate with measured light levels
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
54

## Slide 55
EDITABLE STATE MACHINE
Hysteresis Prevents Chatter
LAMP OFF
raw > 450
DEAD BAND
350-450
LAMP ON
raw < 350
darker
<350
brighter
>450
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
55

## Slide 56
TIMING WAVEFORM
Servo Command Pulse
0 degrees
10%
90 degrees
50%
180 degrees
90%
The Servo library schedules control pulses; servo supply current must not come from an Arduino I/O pin.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
56

## Slide 57
SIGNAL / CONTROL FLOW
Servo Energy and Signal Boundary
1
A0
Potentiometer position
2
map()
0-1023 -> 0-180
3
D9 signal
Timed control pulse
4
5 V supply
Provides actuator energy
5
COMMON GND
Maintains signal reference
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
57

## Slide 58
OBSERVE -> COMPARE -> DECIDE
Analogue Failure Modes
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Stuck 0
Input shorted to GND
ADC trace
Inspect divider
Stuck 1023
Input tied to Vref
ADC trace
Inspect return path
Jitter
Noise / weak supply
Spread over samples
Filter / power
Wrong direction
Divider/map reversed
Endpoint test
Reverse mapping
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
58

## Slide 59
PRACTICE BRIDGE | LO3
Lab 6: LDR Dark-Activated Lamp with Hysteresis
MECHANISM TO PROVE
Convert a light-dependent voltage divider into a stable two-threshold control decision.
DELIVERABLE
A calibrated dark-activated lamp that avoids chatter around the switching threshold.
INPUT
5 V
CONTROL
const uint8_t LDR_PIN = A0;
OUTPUT
Serial output shows plausible 0-1023 readings
VERIFY
Output remains stable inside the hysteresis band
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
59

## Slide 60
OBSERVE -> COMPARE -> DECIDE
Lab 6 Calibration Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Bright
Record ADC high/low
Measured value
Choose orientation
Room
Record midpoint
Measured value
Set dead band
Covered
Record dark endpoint
Measured value
Set ON threshold
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
60

## Slide 61
PRACTICE BRIDGE | LO3
Lab 7: Potentiometer-Controlled Servo
MECHANISM TO PROVE
Map a 10-bit ADC measurement to a bounded servo command while respecting the servo power boundary.
DELIVERABLE
A 0-180 degree servo position controller with clamped input and separate-power guidance.
INPUT
Pot outer pins
CONTROL
#include <Servo.h>
OUTPUT
ADC reading changes smoothly
VERIFY
Board does not reset when servo moves
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
61

## Slide 62
RUNNABLE CODE CONTRACT
Lab 7 ADC-to-Servo Contract
#include <Servo.h> Servo actuator; const uint8_t POT_PIN = A0; const uint8_t SERVO_PIN = 9; void setup() { actuator.attach(SERVO_PIN); Serial.begin(9600); } void loop() { int raw = analogRead(POT_PIN); int angle = constrain(map(raw, 0, 1023, 0, 180), 0, 180); actuator.write(angle); Serial.println(angle); delay(15); }
READ THE EVIDENCE
1
analogRead acquires the 10-bit measurement
2
map converts measurement to command units
3
constrain enforces actuator command bounds
4
Common ground makes the signal meaningful
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
62

## Slide 63
SIGNAL / CONTROL FLOW
Analogue Control Case
1
MEASURE
Potentiometer / LDR
2
CALIBRATE
Real endpoints
3
FILTER
Reduce noise
4
DECIDE
Map or hysteresis
5
ACT
Servo / lamp
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
63

## Slide 64
OBSERVE -> COMPARE -> DECIDE
Topic 3 Verification Matrix
TEST
EXPECTED
OBSERVED
DECISION / ACTION
ADC scale
0-1023 bounded
Serial endpoints
ADC mechanism
LDR control
Stable dark lamp
Threshold trace
Applied sensor
Servo
0-180 bounded
Angle checkpoints
Transducer control
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
64

## Slide 65
04
TOPIC 4
Digital Sensors and Transducers
Digital sensor contracts, trigger/echo timing, distance calculation, timeouts, PIR state, and responsive control
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
65

## Slide 66
TECHNICAL MODEL
Digital Sensor Output Contracts
Binary level
Sensor presents HIGH/LOW relative to logic thresholds.
Pulse width
Information is encoded in how long a signal remains HIGH/LOW.
Serial protocol
Bits are framed with timing, addressing and sometimes checksums.
Library object
A library can abstract timing but errors still require explicit handling.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
66

## Slide 67
SIGNAL / CONTROL FLOW
Ultrasonic Ranging Transaction
1
IDLE LOW
Settle trigger
2
10 us TRIGGER
Start burst
3
40 kHz BURST
Sensor transmits
4
ECHO HIGH
Pulse equals round trip
5
TIMEOUT
Bound missing response
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
67

## Slide 68
WORKED CALCULATION
Time-of-Flight Distance
distance = duration x 0.0343 cm/us / 2
SUBSTITUTE REAL VALUES
1,750 us x 0.0343 / 2 = 30.0 cm
Round trip
Divide by two
Temperature
Sound speed changes slightly
Timeout
0 means no valid echo
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
68

## Slide 69
TIMING WAVEFORM
Trigger and Echo Timing
TRIG 10 us
10%
ECHO 1,750 us
57%
30 ms timeout
92%
pulseIn(ECHO, HIGH, 30000) converts a missing echo into duration == 0 instead of an unbounded wait.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
69

## Slide 70
RUNNABLE CODE CONTRACT
Bounded pulseIn() Measurement
const uint8_t TRIG_PIN = 9; const uint8_t ECHO_PIN = 10; const unsigned long ECHO_TIMEOUT_US = 30000; void setup() { pinMode(TRIG_PIN, OUTPUT); pinMode(ECHO_PIN, INPUT); Serial.begin(9600); } void loop() { digitalWrite(TRIG_PIN, LOW); delayMicroseconds(2); digitalWrite(TRIG_PIN, HIGH); delayMicroseconds(10); digitalWrite(TRIG_PIN, LOW); unsigned long duration = pulseIn(ECHO_PIN, HIGH, ECHO_TIMEOUT_US); if (duration == 0) Serial.println("NO_ECHO"); else { float distanceCm = duration * 0.0343f / 2.0f;
READ THE EVIDENCE
1
2 us LOW establishes a clean trigger edge
2
10 us HIGH starts the ranging cycle
3
30,000 us timeout bounds waiting
4
duration == 0 is a separate fault state
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
70

## Slide 71
TECHNICAL MODEL
Ultrasonic Measurement Limits
Blind zone
Very near targets may not produce a usable separated echo.
Surface angle
A slanted target reflects energy away from the receiver.
Material
Soft or irregular surfaces absorb/scatter ultrasound.
Cross-talk
Nearby ultrasonic sensors can hear another transmitter.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
71

## Slide 72
SIGNAL / CONTROL FLOW
PIR Motion Contract
1
WARM-UP
Sensor stabilises
2
IDLE
OUT LOW
3
MOTION
OUT HIGH
4
HOLD TIMER
Extend on new motion
5
EXPIRE
Return light LOW
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
72

## Slide 73
TECHNICAL MODEL
Digital Sensor Noise Controls
Pull-up/down
Defines idle voltage when output is open or high impedance.
Debounce
Rejects rapid contact transitions.
Timeout
Bounds missing pulses or stalled devices.
State machine
Separates warm-up, active, hold and fault behaviour.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
73

## Slide 74
DECISION / COMPARISON
delay() Hold vs millis() Hold
BLOCKING HOLD
Control
delay(5000)
Effect
No normal sensor/serial work
Retrigger
Cannot extend cleanly
Use
Simple one-shot demo
RESPONSIVE HOLD
Control
elapsed < HOLD_MS
Effect
Loop remains responsive
Retrigger
Update lastMotionMs
Use
Real motion light
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
74

## Slide 75
EDITABLE STATE MACHINE
Obstacle Indicator States
CLEAR
green
NEAR
red
NO ECHO
fault
> limit
<= limit
timeout
valid
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
75

## Slide 76
PRACTICE BRIDGE | LO4
Lab 8: Ultrasonic Distance with Timeout
MECHANISM TO PROVE
Measure echo pulse width, convert time-of-flight to distance, and handle a missing echo safely.
DELIVERABLE
A distance monitor that reports centimetres or NO_ECHO within a bounded 30 ms wait.
INPUT
Sensor VCC
CONTROL
const uint8_t TRIG_PIN = 9;
OUTPUT
Distance is within a reasonable tolerance of the ruler
VERIFY
No divide-by-zero or indefinite wait occurs
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
76

## Slide 77
RUNNABLE CODE CONTRACT
Lab 8 Distance Evidence
const uint8_t TRIG_PIN = 9; const uint8_t ECHO_PIN = 10; const unsigned long ECHO_TIMEOUT_US = 30000; void setup() { pinMode(TRIG_PIN, OUTPUT); pinMode(ECHO_PIN, INPUT); Serial.begin(9600); } void loop() { digitalWrite(TRIG_PIN, LOW); delayMicroseconds(2); digitalWrite(TRIG_PIN, HIGH); delayMicroseconds(10); digitalWrite(TRIG_PIN, LOW); unsigned long duration = pulseIn(ECHO_PIN, HIGH, ECHO_TIMEOUT_US); if (duration == 0) Serial.println("NO_ECHO"); else { float distanceCm = duration * 0.0343f / 2.0f;
READ THE EVIDENCE
1
TRIG and ECHO have distinct directions
2
Echo time is unsigned long microseconds
3
Formula divides round-trip path by two
4
NO_ECHO is not treated as zero distance
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
77

## Slide 78
OBSERVE -> COMPARE -> DECIDE
Lab 8 Acceptance Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
20 cm
Approx 20 cm
Serial + ruler
Within tolerance
80 cm
Approx 80 cm
Serial + ruler
Within tolerance
No target
NO_ECHO
Serial state
Timeout handled
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
78

## Slide 79
PRACTICE BRIDGE | LO4
Lab 9: PIR Motion-Activated Light
MECHANISM TO PROVE
Use a digital motion sensor contract and a non-blocking hold timer to control a light.
DELIVERABLE
A motion light that extends its ON period when new motion arrives and expires safely after five seconds.
INPUT
PIR VCC
CONTROL
const uint8_t PIR_PIN = 2;
OUTPUT
Motion drives the output HIGH
VERIFY
loop() remains responsive without delay(5000)
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
79

## Slide 80
EDITABLE STATE MACHINE
Lab 9 Motion-Light Control
OFF
no recent motion
ON
motion seen
EXTENDED
new motion
EXPIRED
5 s elapsed
PIR HIGH
PIR HIGH
time
reset
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
80

## Slide 81
OBSERVE -> COMPARE -> DECIDE
Lab 9 Acceptance Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Warm-up
Stable idle LOW
Observed OUT
Ready
Motion
Light HIGH
LED evidence
Sensor detected
Retrigger
Hold extends
Timestamp trace
Non-blocking
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
81

## Slide 82
OBSERVE -> COMPARE -> DECIDE
Digital Sensor Fault Isolation
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Power
Correct VCC/GND
Meter / module LED
Fix supply
Signal
Expected HIGH/LOW/pulse
Serial/raw trace
Fix pin/threshold
Timing
Within protocol window
Logic/waveform
Fix timeout/edge
Control
State transition correct
Output evidence
Fix decision logic
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
82

## Slide 83
TECHNICAL MODEL
Digital Sensor Decision Rules
Know the encoding
Level, pulse width, serial frame, or library abstraction.
Bound every wait
A failed sensor must not freeze the control loop.
Represent faults
NO_ECHO/READ_ERROR are states, not plausible measurements.
Verify with references
Compare sensor evidence against a ruler, known motion, or protocol timing.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
83

## Slide 84
05
TOPIC 5
Actuators
Actuator energy boundaries, motor drivers, flyback protection, steppers, DHT validation, and feedback control
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
84

## Slide 85
SIGNAL / CONTROL FLOW
Actuator Control Architecture
1
MEASUREMENT
Sensor value + validity
2
DECISION
Threshold/state/controller
3
LOGIC DRIVE
GPIO or PWM
4
POWER STAGE
MOSFET / driver array
5
ACTUATOR
Motion / light / sound
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
85

## Slide 86
TECHNICAL MODEL
Why Motors Need a Driver
Current
Motor startup/stall current exceeds an I/O pin's safe capability.
Inductance
Switch-off generates a voltage spike that can damage electronics.
Noise
Brushes and current steps disturb supply and sensor signals.
Isolation of roles
GPIO commands; the driver and external supply deliver energy.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
86

## Slide 87
SIGNAL / CONTROL FLOW
Protected DC Motor Path
1
D5 PWM
Control duty
2
GATE RESISTOR
Limit edge current
3
MOSFET
Low-side switch
4
FLYBACK DIODE
Clamp inductive kick
5
MOTOR SUPPLY
Deliver load current
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
87

## Slide 88
TIMING WAVEFORM
PWM Motor Command
STOP
2%
LOW SPEED
35%
MEDIUM
60%
FULL
98%
Commanded duty controls average drive, but actual speed depends on load, supply, motor characteristics and the driver's losses.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
88

## Slide 89
TECHNICAL MODEL
Stepper Position Mechanism
Phase sequence
Coils energise in a defined order to create incremental motion.
Step count
Position is inferred from commanded steps when no steps are missed.
Speed/torque tradeoff
Excessive step rate causes vibration or lost steps.
Driver array
ULN2003 channels sink coil current and include protection diodes.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
89

## Slide 90
SIGNAL / CONTROL FLOW
ULN2003 Stepper Boundary
1
D8-D11
Four logic phases
2
IN1-IN4
Driver inputs
3
DARLINGTON
Current amplification
4
COM DIODES
Inductive protection
5
28BYJ-48
Geared position output
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
90

## Slide 91
TECHNICAL MODEL
DHT11 Transaction and Validity
Command/read
The library manages the sensor's timing-sensitive exchange.
Sample interval
The device is slow; repeated reads must respect its timing.
NaN
A failed transaction is not a temperature or humidity value.
Control gate
Actuator decisions run only when the measurement is valid.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
91

## Slide 92
RUNNABLE CODE CONTRACT
Reject Invalid Measurements
float t = dht.readTemperature(); float h = dht.readHumidity(); if (isnan(t) || isnan(h)) { Serial.println("READ_ERROR"); return; } // Only valid values reach control logic.
READ THE EVIDENCE
1
Acquire both measurements
2
isnan() detects failed conversion
3
Fault state is reported explicitly
4
return prevents unsafe false control
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
92

## Slide 93
EDITABLE STATE MACHINE
Fan Hysteresis Controller
FAN OFF
T < 30 C
FAN ON
T >= 30 C
HOLD ON
28-30 C
FAN OFF
T <= 28 C
warm
cool slightly
cool
warm
A state machine makes every output, entry condition, exit condition, and safe default inspectable.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
93

## Slide 94
OBSERVE -> COMPARE -> DECIDE
Actuator Failure Modes
TEST
EXPECTED
OBSERVED
DECISION / ACTION
No motion
No supply/drive
Measure supply/gate
Fix power stage
Resets
Supply dip/noise
Serial reset trace
Separate/decouple
Hot driver
Wrong device/current
Temperature/current
Reduce load
Lost steps
Rate too high
Position error
Lower speed
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
94

## Slide 95
PRACTICE BRIDGE | LO5
Lab 10: DHT11 Temperature and Humidity Monitor
MECHANISM TO PROVE
Read a library-managed digital sensor transaction and reject invalid measurements before control use.
DELIVERABLE
A one-hertz temperature/humidity monitor that identifies NaN failures instead of treating them as real values.
INPUT
DHT VCC
CONTROL
#include <DHT.h>
OUTPUT
Temperature and humidity update approximately once per second
VERIFY
dht.begin() is called in setup()
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
95

## Slide 96
OBSERVE -> COMPARE -> DECIDE
Lab 10 DHT Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Room
Plausible T/RH
Serial trace
Valid
Warm
Temperature rises
Serial trace
Sensor responds
Data open
READ_ERROR
Fault trace
Invalid rejected
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
96

## Slide 97
PRACTICE BRIDGE | LO5
Lab 11: Stepper Motor Position Control
MECHANISM TO PROVE
Drive a four-phase stepper through a transistor array and relate commanded steps to angular position.
DELIVERABLE
A 28BYJ-48/ULN2003 actuator that moves one revolution forward and backward at a bounded speed.
INPUT
D8-D11
CONTROL
#include <Stepper.h>
OUTPUT
Motor completes a forward and reverse move
VERIFY
Grounds are common and board remains stable
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
97

## Slide 98
SIGNAL / CONTROL FLOW
Lab 11 Phase-to-Position Chain
1
STEPS
+2048 / -2048
2
LIBRARY
Phase order
3
ULN2003
Coil current
4
GEARBOX
Mechanical reduction
5
EVIDENCE
Marked shaft position
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
98

## Slide 99
OBSERVE -> COMPARE -> DECIDE
Lab 11 Acceptance Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
Forward
One revolution
Shaft mark
Position close
Reverse
Return to origin
Shaft mark
Direction proven
Higher speed
Possible missed steps
Position error
Set safe rate
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
99

## Slide 100
PRACTICE BRIDGE | LO5
Lab 12: DHT Fan Controller with Hysteresis
MECHANISM TO PROVE
Integrate measurement, decision logic, and a protected continuous-drive actuator into a feedback controller.
DELIVERABLE
A temperature-controlled DC fan with MOSFET switching, flyback protection, PWM drive, and hysteresis.
INPUT
DHT DATA
CONTROL
#include <DHT.h>
OUTPUT
Fan turns ON above 30 C
VERIFY
Motor current never flows through an Arduino I/O pin
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
100

## Slide 101
RUNNABLE CODE CONTRACT
Lab 12 Feedback Controller
#include <DHT.h> const uint8_t DHT_PIN = 2; const uint8_t FAN_PWM_PIN = 5; const float FAN_ON_C = 30.0; const float FAN_OFF_C = 28.0; DHT dht(DHT_PIN, DHT11); bool fanOn = false; void setup() { pinMode(FAN_PWM_PIN, OUTPUT); Serial.begin(9600); dht.begin(); } void loop() { float t = dht.readTemperature(); if (isnan(t)) { Serial.println("READ_ERROR"); delay(2000); return; } if (!fanOn && t >= FAN_ON_C) fanOn = true;
READ THE EVIDENCE
1
Invalid sensor value exits before control
2
Separate ON/OFF thresholds prevent chatter
3
PWM pin commands the MOSFET, not the motor directly
4
Serial trace records measurement and actuator state
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
101

## Slide 102
OBSERVE -> COMPARE -> DECIDE
Lab 12 Acceptance Evidence
TEST
EXPECTED
OBSERVED
DECISION / ACTION
>=30 C
Fan ON
T/FAN trace
Control enters ON
28-30 C
Hold prior state
T/FAN trace
Hysteresis
<=28 C
Fan OFF
T/FAN trace
Control exits ON
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
102

## Slide 103
OBSERVE -> COMPARE -> DECIDE
Course Verification Matrix
TEST
EXPECTED
OBSERVED
DECISION / ACTION
LO1
Board/serial mechanism
Labs 1-2
Topic 1
LO2
Safe circuits/input/PWM
Labs 3-5
Topic 2
LO3
ADC/LDR/servo
Labs 6-7
Topic 3
LO4
Ultrasonic/PIR
Labs 8-9
Topic 4
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
103

## Slide 104
CLOSE-OUT
Course Feedback
Course evaluation
Complete the feedback form in LMS/TMS.
Your comments
Tell the trainer what worked and what to improve.
Completion
Confirm the portal records your feedback.
Support
Keep the Learner Guide and labs for post-course practice.
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
104

## Slide 105
AFTER-CLASS HELP
Support
Email
enquiry@tertiaryinfotech.com
Telephone
+65 6100 0613
Course portal
https://lms-tms.tertiaryinfotech.com/
Arduino reference
https://docs.arduino.cc/language-reference/
Arduino Masterclass | C218
Tertiary Infotech Academy Pte Ltd | UEN 201200696W
105

## Slide 106
SENSE | DECIDE | ACT | VERIFY
Thank You
A working prototype is a claim. A measured, repeatable acceptance test is evidence.
Arduino Masterclass | C218 | Version 1.0